## Slide 1
第三組
109302526 李宗霖 109302512 陳泰安
111322089 黃亭耀 112322022 郭瑞嫻
109302516 劉晏彤 109302519 目崎勇太
Final Project on the Finite Element Method course in the first semester of the 112 academic year
Final Project on the Finite Element course
RC Column Plastic Hinge Blind Prediction

## Slide 2: Why we need to analyze the structure?
2
Final report on the Finite Element Method course in the first semester of the 112 academic year
Taiwan seismic zone
  Taiwan gets hit by earthquakes a lot, so it's important to keep an eye on seismic activity and research here.
Taiwan lies within the Pacific Ring of Fire and at the junction of the Eurasian Plate and the Philippine Sea Plate.

## Slide 3: Compare two analysis software?
3
Final report on the Finite Element Method course in the first semester of the 112 academic year
 | SAP2000 | ABAQUS
ADVANTAGES | 1. Easy to use and learn 2. In some case, SAP2000's analysis speed might be faster than ABAQUS | 1. The most reliable analysis results 2. The strongest problem-solving capability
DIS-ADVANTAGES | 1. It might not be as useful as ABAQUS in handling complex problems 2. Hard to solve the Nonlinear and nonstructural dynamics | 1. When dealing with complex problems, it requires more time 2. Maybe hard to use and learn

## Slide 4: How to analyze the structure?
Outline
Why we use
Plastic Hinges
How to simulate
Plastic Hinges
Takeda Model
4
Final report on the Finite Element Method course in the first semester of the 112 academic year
Notes: Hello, everyone my name is. In my section, I will introduce how to analyze the building structure.
Everyone should be familiar with this picture. It is the teaching and research building of our school. As a student in the structure group, I will think about how this building was built? A very important knowledge point among them is the plastic hinge.

## Slide 5
Why we use Plastic Hinge
1999 Chi-Chi earthquake
2023 Turkey earthquake
Outline
Why we use
Plastic Hinges
How to simulate
Plastic Hinges
Reinforced concrete (RC) buildings are designed to allow plastic hinges due to cost-effectiveness and safety considerations.
5
Final report on the Finite Element Method course in the first semester of the 112 academic year
Takeda Model
Notes: Reinforced concrete (RC) buildings are designed to allow plastic hinges due to cost-effectiveness and safety considerations.
However, it is possible that due to improper analysis, these building were severely damaged and collapsed in past earthquakes.

## Slide 6
Why we use Plastic Hinge
Ductile Design
How to accurately simulate the plastic hinges of beams and columns to express their behavior from linear to nonlinear, as well as the stiffness and strength of the overall structure.
2500 years Return Period
Allowable Ductility Capacity Ra
475 years Return Period
Ductility Capacity R
Strong Column and Weak Beam
Foundation
Column
Beam
6
Final report on the Finite Element Method course in the first semester of the 112 academic year
Notes: To discuss this issue, we first introduce the design process of the building.
First of all, the building design adopts Ductile design and based on the concept of strong columns and weak beams. Because if the column enters the plastic hinge first, it will cause structural collapse. Finally, the design will be based on the design and maximum earthquake force.
So that's why we use plastic hinges to analysis building.

## Slide 7: How to simulate Plastic Hinges
Outline
Why we use
Plastic Hinges
How to simulate
Plastic Hinges
Foundation
The main challenges to simulate the collapse capacity of a building is to analysis the hysteresis behavior of various structural members.
Column
Beam
hysteresis behavior ?
7
Final report on the Finite Element Method course in the first semester of the 112 academic year
Takeda Model

## Slide 8: How to simulate Plastic Hinges
The hysteresis behavior of reinforced concrete columns in the
plastic hinge zone can be determined through experiments
and finite element analysis software (ABAQUS).
Column Data
Experiment or FEA
Column hysteresis loop
8
Final report on the Finite Element Method course in the first semester of the 112 academic year

## Slide 9: How to simulate Plastic Hinges
It is impossible to repeat the experiment or analyze it through FEA software just to analyze the hysteresis loop of a column.
Therefore, in practice, usually use a centralized plastic hinge model to simulate the behavior of beam-column structures after stress.
Nonlinear simulation model
Ground motion intensity measure (IM)
Deterioration of Stiffness and Strength
To evaluate the seismic risk of building :
Human casualties
＆ Dollar losses
9
Final report on the Finite Element Method course in the first semester of the 112 academic year

## Slide 10
Outline
Why we use
Plastic Hinges
How to simulate
Plastic Hinges
Takeda Model
Takeda Hysteresis Model
10
Final report on the Finite Element Method course in the first semester of the 112 academic year
Column
Beam
Column hysteresis loop
From experiment
Nonlinear simulation model

## Slide 11
Takeda Hysteresis Model
Takeda Hysteresis Model simplifies analysis, requiring fewer parameters, and suits concrete structures well. With lower energy dissipation than dynamic models, it adeptly captures structural hysteresis under various loads.
11
Final report on the Finite Element Method course in the first semester of the 112 academic year
: elastic stiffness
: unloading stiffness
: yielding displacement
: displacement (the structure is cracked)
: maximum displacement
: yielding restoring force
: restoring force (the structure is cracked)
: stiffness degradation coefficient

## Slide 12
1. Use Takeda Model to simulate all structure component hysteresis.
3. Accurately simulate the dynamic response of structures.
2. Import them into FEA software and combine them for analysis.
SAP2000
12

## Slide 13
SAP2000 Simulation
13
Final report on the Finite Element Method course in the first semester of the 112 academic year
Outline
Define materials
Define cyclic load
Define plastic hinge
Simulate the
response of structures

## Slide 14
SAP2000 Simulation
14
Final report on the Finite Element Method course in the first semester of the 112 academic year
Outline
Define materials
Define cyclic load
Define plastic hinge
Simulate the
response of structures
Refer to the table and define materials
  Concrete properties
  Rebar properties

## Slide 15
SAP2000 Simulation - Define materials
15
Final report on the Finite Element Method course in the first semester of the 112 academic year
Definition of material parameters according to the table
 | SD280W
Yield strength (fy) | 351.48
Tensile strength (fu) | 462.356

## Slide 16
SAP2000 Simulation - Define materials
16
Final report on the Finite Element Method course in the first semester of the 112 academic year
Definition of material parameters according to the table

## Slide 17
SAP2000 Simulation
17
Final report on the Finite Element Method course in the first semester of the 112 academic year
Outline
Define materials
Define cyclic load
Define plastic hinge
Simulate the
response of structures
Defining Cyclic Load by Time History Function

## Slide 18
SAP2000 Simulation - Define cyclic load
18
Final report on the Finite Element Method course in the first semester of the 112 academic year
Defining Cyclic Load by Time History Function
Applied to the model

## Slide 19
SAP2000 Simulation
19
Final report on the Finite Element Method course in the first semester of the 112 academic year
Outline
Define materials
Define cyclic load
Define plastic hinge
Simulate the response of structures
Use the parameters of plastic hinges from the literature
Is the result reasonable?
Simulate the response of structures
NO
YES
Flow Chart
Identify and solve modeling problems
Calculation of plastic hinge parameters
Simulate the response of structures
Is the result reasonable?
Identify and solve plastic hinge parameters problems
Complete the analysis
YES
NO
Notes: Before calculating the plastic hinges for this RC column, use the plastic hinge parameters from the literature to test if the model is OK.
After confirming that the model is OK, the plastic hinge parameters for this RC column are calculated.
The simulation is divided into two parts to identify the source of the problem.
To see whether the problem is from model or parameters.

## Slide 20
SAP2000 Simulation
20
Final report on the Finite Element Method course in the first semester of the 112 academic year
Flow Chart
Refer to the literature for the proposed definition of plastic hinges and quote the parameters of plastic hinges from the literature to test the model.
References:
Yu-Chi Sung ·2004 · A STUDY ON PUSHOVER ANALYSIS OF REINFORCED CONCRETE COLUMNS Journal of Architecture, No. 46, PP.47~65, April. 2004
Use the parameters of plastic hinges from the literature
Is the result reasonable?
Simulate the response of structures
NO
Identify and solve modeling problems

## Slide 21
SAP2000 Simulation
21
Final report on the Finite Element Method course in the first semester of the 112 academic year
Flow Chart
References:
Yu-Chi Sung ·2004 · A STUDY ON PUSHOVER ANALYSIS OF REINFORCED CONCRETE COLUMNS Journal of Architecture, No. 46, PP.47~65, April. 2004
Use the parameters of plastic hinges from the literature
Is the result reasonable?
Simulate the response of structures
NO
Identify and solve modeling problems
Notes: This is the simulation result of plastic hinge

## Slide 22
SAP2000 Simulation
22
Final report on the Finite Element Method course in the first semester of the 112 academic year
Flow Chart
References:
Yu-Chi Sung ·2004 · A STUDY ON PUSHOVER ANALYSIS OF REINFORCED CONCRETE COLUMNS Journal of Architecture, No. 46, PP.47~65, April. 2004
Use the parameters of plastic hinges from the literature
Is the result reasonable?
Simulate the response of structures
NO
Identify and solve modeling problems
Unit:mm
Unit:KN
Notes: This is the simulation result of Hysteresis loop

## Slide 23
SAP2000 Simulation
23
Final report on the Finite Element Method course in the first semester of the 112 academic year
Flow Chart
References:
Yu-Chi Sung ·2004 · A STUDY ON PUSHOVER ANALYSIS OF REINFORCED CONCRETE COLUMNS Journal of Architecture, No. 46, PP.47~65, April. 2004
Use the parameters of plastic hinges from the literature
Is the result reasonable?
Simulate the response of structures
NO
Identify and solve modeling problems
Notes: Next, we need to determine if the simulation results are correct.
It can be noticed that the plastic hinge deterioration does not follow the backbone curve.

## Slide 24
SAP2000 Simulation
24
Final report on the Finite Element Method course in the first semester of the 112 academic year
Flow Chart
References:
Yu-Chi Sung ·2004 · A STUDY ON PUSHOVER ANALYSIS OF REINFORCED CONCRETE COLUMNS Journal of Architecture, No. 46, PP.47~65, April. 2004
Use the parameters of plastic hinges from the literature
Is the result reasonable?
Simulate the response of structures
NO
Identify and solve modeling problems
Hysteresis loop is weird.
Notes: Since the plastic hinge deterioration does not follow the curve of the backbone, the hysteresis loop is also problematic.
You can see there's a big jump here.

## Slide 25
SAP2000 Simulation
25
Final report on the Finite Element Method course in the first semester of the 112 academic year
Flow Chart
Use the parameters of plastic hinges from the literature
Is the result reasonable?
Simulate the response of structures
NO
Identify and solve modeling problems
Calculation of plastic hinge parameters
Simulate the response of structures
Is the result reasonable?
Identify and solve plastic hinge parameters problems
Complete the analysis
YES
NO
Notes: I've tried a lot of things, but I haven't solved the problem by the deadline.
So the flowchart stops here and I hope to solve the problem later when I am more familiar with SAP2000.

## Slide 26: Part-Concrete
26
Final report on the Finite Element Method course in the first semester of the 112 academic year

## Slide 27: Part-Vertical reinforcement
27
112學年第一學期有限元素法課程期末專題報告
27
Final report on the Finite Element Method course in the first semester of the 112 academic year

## Slide 28: Part-stirrup
28
112學年第一學期有限元素法課程期末專題報告
28
Final report on the Finite Element Method course in the first semester of the 112 academic year

## Slide 29: Part-stirrup
29
112學年第一學期有限元素法課程期末專題報告
29
Final report on the Finite Element Method course in the first semester of the 112 academic year

## Slide 30: Material
30
112學年第一學期有限元素法課程期末專題報告
30
Final report on the Finite Element Method course in the first semester of the 112 academic year

## Slide 31: Assembly
31
112學年第一學期有限元素法課程期末專題報告
31
Final report on the Finite Element Method course in the first semester of the 112 academic year

## Slide 32: Assembly
32
112學年第一學期有限元素法課程期末專題報告
32
Final report on the Finite Element Method course in the first semester of the 112 academic year

## Slide 33: Step
33
112學年第一學期有限元素法課程期末專題報告
33
Final report on the Finite Element Method course in the first semester of the 112 academic year

## Slide 34: Interaction
34
112學年第一學期有限元素法課程期末專題報告
34
Final report on the Finite Element Method course in the first semester of the 112 academic year

## Slide 35: Load-B.C&Displacement
35
112學年第一學期有限元素法課程期末專題報告
35
Final report on the Finite Element Method course in the first semester of the 112 academic year

## Slide 36: Load-Amplitude
36
112學年第一學期有限元素法課程期末專題報告
36
Final report on the Finite Element Method course in the first semester of the 112 academic year

## Slide 37: Mesh
37
112學年第一學期有限元素法課程期末專題報告
37
Final report on the Finite Element Method course in the first semester of the 112 academic year

## Slide 38: Mesh
38
112學年第一學期有限元素法課程期末專題報告
38
Final report on the Finite Element Method course in the first semester of the 112 academic year

## Slide 39: Job
39
112學年第一學期有限元素法課程期末專題報告
39
Final report on the Finite Element Method course in the first semester of the 112 academic year

## Slide 40: Job-Total increment
40
112學年第一學期有限元素法課程期末專題報告
40
Final report on the Finite Element Method course in the first semester of the 112 academic year

## Slide 41: Visualization-Stress
41
112學年第一學期有限元素法課程期末專題報告
41
Final report on the Finite Element Method course in the first semester of the 112 academic year

## Slide 42: Visualization-Bottom shear
42
112學年第一學期有限元素法課程期末專題報告
N571
42
Final report on the Finite Element Method course in the first semester of the 112 academic year

## Slide 43: Visualization-Reinforcement
43
112學年第一學期有限元素法課程期末專題報告
Entering the plastic stage
43
Final report on the Finite Element Method course in the first semester of the 112 academic year
Notes: 在500秒時底部鋼筋進入塑性階段

## Slide 44: Visualization-Top displacement
44
112學年第一學期有限元素法課程期末專題報告
N433
44
Final report on the Finite Element Method course in the first semester of the 112 academic year

## Slide 45: Visualization-Hysteresis loop
45
112學年第一學期有限元素法課程期末專題報告
45
Final report on the Finite Element Method course in the first semester of the 112 academic year